## Slide 1: Independent Meeting (08/14/2023)
Amar Maksumić

## Slide 2: Table of Contents
SavGol filter
Finding range of bands
Remaining Chips

## Slide 3: SavGol Filter
Savitzky Golay Filter is a digital signal processing technique used for smoothing or noise reduction of a dataset
It's particularly useful for data that may have some level of noise or variation that needs to be reduced while preserving the general trends or features of the signal.
There are 5 key steps to the filter => next slide

## Slide 4: SavGol Filter (step 1)
Window Selection: Choose a window size and a polynomial order
  Window size determines number of neighboring points around the current point to include in smoothing
  Polynomial order determines the degree of the polynomial used for the regression being performed on these points.

## Slide 5: SavGol Filter (step 2)
Window Sliding: “Slide” the chosen window over the data in the dataset.
  Each time we slide it over 1 unit, this new set of points local to the window is the mini-dataset we will perform the next operation to.

## Slide 6: SavGol Filter (step 3)
Polynomial Fitting: On the local set of data points from the last slide, fit a polynomial to these local data points.
  The degree of the polynomial is equal to the degree from step 1

## Slide 7: SavGol Filter (step 4)
Regression: Once you fit the polynomial to the local set of data points in the window, evaluate the polynomial at the center of the window.
  This gives the smoothed value for that single data point.

## Slide 8: SavGol Filter (step 5)
Repeat: slide the window one data point unit at a time and repeat the process for the entire dataset.

## Slide 9: Finding Range of Bands
Find ___ in lower and upper quartiles of each graph, and use these to determine the halfway point on each of the rising / falling edges
  Average?
  Median?